## Slide 1: NETWORKING BASICS 2

## Slide 2: SWITCHING

## Slide 3: Layer 2 basics
Builds and maintains a MAC address table used for forwarding packets
Switch stores the source mac address and the port number that it receives a packet

## Slide 4: ARP
Address Resolution Protocol helps to determine the MAC address of the destination host before forwarding
Computers and Routers maintains an ARP table
Uses broadcast to learn the destination mac address

## Slide 5: VLAN Foundations
Logically groups users
Segments broadcast domains
Subnet correlation
Access control
Quality of Service

## Slide 6: Trunk Links
VLANs can span across multiple switches with a help of Trunk links
Places a unique identifier in header of each frame
Functions at Layer 2
Each logical VLAN is like a separate switch
Trunking protocols: ISL and 802.1q

## Slide 7: ISL Encapsulation
Cisco proprietary

## Slide 8: 802.1q Tagging
Industry standard

## Slide 9: Native VLAN

## Slide 10: Inter VLAN Routing
Router on a stick
Subinterfaces (logical) are created for the physical interface
802.1q tagging is configured

## Slide 11: ROUTING

## Slide 12: How routing works?
To reach anything that is outside the local network
Routers maintains a routing table
A route entry typically contains destination network, subnet mask, next hop address, administrative distance, metric

## Slide 13: Types of Routing Protocols
Static routing
Dynamic routing
Dynamic Routing

## Slide 14: Static Routing
Routes are configured manually
Route entry always stays on the routing table regardless of the state of the destination network

## Slide 15: RIP version 1
Advertises only classfull networks like 10.0.0.0/8, 150.16.0.0/16, 195.20.32.0/24
Subnet mask is not included in the routing update
No authentication
Uses broadcast address to advertise networks
Determines shortest path based on hop-counts (metric)
Update timer: Routing updates sent every 30s
Invalid timer: Route is marked as invalid (hop-count=16) when no update is heard in 180s
Flush timer: Time between route is invalidated and removal of entry from the routing table which is 60s Hold-down timer: 180s, allows route to get stabilized

## Slide 16: RIP version 2
Timers are same as RIPv1
Supports classless network like 10.10.1.0/24, 172.30.17.86/23, 182.73.23.0/30
Sends out subnet mask in the updates
Adds authentication
Uses multicast for updates, 224.0.0.9

## Slide 17: THANK YOU