NETWORKING BASICS 5

---
OSPF

---
Open Shortest Path First (OSPF)
Maintains 3 tables:
  - Neighbor table
  - Topology table
  - Routing table
Triggered updates are sent
Also sends periodic updates on longer intervals
Uses the topology table and updates the routing table
Network is structured into routing areas to simplify administration, optimize traffic and resource utilization
Requires an hierarchical design (upon IP schema)

---
OSPF network

---
OSPF packet types
HELLO
Database description (DBD)
Link-State Request (LSR)
Link-State Advertisement (LSA)
Link-State Update (LSU)
Link-State Acknowledgement (LSACK)

---
HELLO packet
Router ID
Hello/Dead interval*
Network mask*
Neighbors
Area ID*
Router priority
DR IP address
BDR IP address
Authentication password
Password
Stub Area Flag*
Hello timer
10 sec (Broadcast/P2P networks)
30 sec (NBMA networks)
Dead timer = 4 x hello timer

---
Router ID
Determines its router ID (32-bit address)
  - Simply the router's name in the OSPF process
  - Highest active interface IP address when OSPF process starts (Loopback interfaces beat physical interfaces)
OSPF router ID only changes when OSPF process is restarted (reset) or the router is rebooted
Best practice is to manually configure a router ID

---
Understanding OSPF neighbor relationships
DOWN: No hello received from the neighbor
INIT: The hello is seen from the neighbor
2-WAY: The router has seen its own router ID on the neighbor field in its received hello packet
EXSTART/EXCHANGE: Seen when neighbors trying to exchange DBD (Database description) packets
LOADING: Router sends/receive LSR (Link state request) packets and LSU (Link state update)
FULL: Good state ! Neighbors are synchronized !!

---
Full relationship process

---
OSPF Cost
Cost = 100 / Bandwidth in Mbps
Common costs
  - 56Kbps > 1785
  - 64Kbps > 1562
  - T1 (1.544Mbps) > 65
  - E1 (2.048 Mbps) > 48
  - Ethernet (10Mbps) > 10
  - Fast ethernet (100Mbps) > 1

---
Understanding the DR and BDR
Designated Router (DR) and Backup Designated Router (BDR)
On a shared network, one of them will be elected as DR and another as BDR
Router with highest priority (or) router ID will become the DR
Router priority is 1 by default
There is no DR/BDR on P2P network
Uses multicast 224.0.0.6 for updating DR/BDR
Uses multicast 224.0.0.5 for updating other neighbors
On a shared ethernet network, a maximum of only 2 FULL state relationship can be found

---
OSPF network types
Broadcast, multi-access networks
  - Eg. Ethernet, Token ring
  - Single operation mode
  - DR/BDR election
Point-to-point networks
  - Eg. T1, CAS, ISDN BRI/PRI
  - Single operation mode
  - No BDR/DR
Non-Broadcast Multi-Access (NMBA) networks
  - Eg. Frame-relay, ATM
  - Five modes of operation

---
NBMA modes
Non-Broadcast (NBMA) - RFC standard
Point-to-multipoint - RFC standard
Point-to-point - Cisco proprietary
Broadcast - Cisco proprietary
Point-to-multipoint, Non-broadcast - Cisco proprietary

---
Understanding LSA types
LSA type 1: Router LSA
LSA type 2: Network LSA (DR generated)
LSA type 3: Summary LSA (ABR summary route)
LSA type 4: Summary LSA (ASBR location)
LSA type 5: External LSA (ASBR summary route)

---
OSPF area types
Backbone Area (Area 0)
Stub area
Not-so-stubby area
Totally stubby area
Not-so-totally-stubby area